## Slide 1: Elektrický koncept robotického pracoviska ME-Inspection SK
PM000932
Q345/2019/01
26. 08. 2019, Version 1.0
Prepared by: Marian Sramek

## Slide 2
Version
Version | Description of change | Person
1.0 | Creation of document | Marian Sramek

## Slide 3
Electrical concept: Main cabinet, TIA portal concept
Profinet
LCC iPC
Remote access / plant network
Datalogic M410
SIMATIC IFP1900 PRO 19”
Flat panel monitor
(Continental version)
6AV7466-6MA02-0CS0
HW PLC
CPU 1518F-4 PN/DP
6ES7318-3FL01-0AB0
(PROFIsafe, SIMATIC ProDiag S7-1500, Runtime License(s))
Runtime software
SIMATIC WinCC Runtime Advanced V15
SIMATIC NET PC Software V15 SOFTNET-IE S7
(OPC UA/DA server)
Windows 10 IoT Enterprise
SIMATIC ProDiag for WinCC Runtime Advanced, Controls
SIMATIC IPC427E
64 Bit Version
6AG4141-5BG47-0FA0

## Slide 4
Electrical concept: Option #1 - Main cabinet LCC iPC
LCC iPC
Flat Panel IFP1900 PRO
6AV7863-3MA16-1AA0
SIMATIC IPC427E
64 Bit Version
6AG1141-5BG37-4FA0

## Slide 5
Electrical concept: Main cabinet
1FK7080-2AF71-1CG0
Machine conveyor
1FK7034-2AK71-1CA0
Marker conveyor
CH092A-11-1105
Kollmorgen
Spindle motor
1FK7103-2AF71-1BB0
Upper tooling
Delivery of new motors and cables. Gears, pulleys, installation and adaption is not part of delivery!
All origin parts will
be reused
ET200SP
Sinamics S120

## Slide 6
Electrical concept: Main cabinet
Machine conv
Width adjust
0,25kW
Infeed roller
0,25kW
Contact control
Lubber tire rotation
0,12kW
Lubber tire rotation
0,12kW
All motors, gears, pulleys are not part of delivery! Reused origin ones.
ET200SP
Sinamics S120
Sorter conveyor
Sorter lift
All motors, gears, pulleys are not part of delivery! Reused origin ones.

## Slide 7
Electrical concept: Lubrification station
Matrix M410
Ethernet
communication
ET200SP
Delivery of plant

## Slide 8
Electrical concept: Service, marker conveyor and lift
ET200SP